## Slide 1: CN
Dr. Minal Moharir

## Slide 2: Efficiency of Asynchronous Transmission
Example: Determine the efficiency of 20KB data transmission using Asynchronous transmission method.
Solution:
Actual data = 20KB=20×8Kb=160Kb=1000×160b=160000 bit
Overhead data bit required for each group of 8 bit = 3 bit
Total bits = Actual data bit + overhead data bits = 160000 bit + 60000 bit = 220000 bit
So, Efficiency = (160000/220000) × 100% = 73%

## Slide 3: Efficiency of Synchronous Transmission
Example: Determine the efficiency of 20KB data transmission using Synchronous transmission method.
Solution:
Actual data = 20KB=20×8Kb=160Kb=1000×160b=160000 bit
Suppose, a block having 80 characters, So block size = 80×8 bit = 640 bit
Overhead data bit required for each block of 640 bit group = 32 bit
So Total overhead data bits required for 160000 bit data transmission = (32/640)× 160000 = 8000 bit
Total bits = Actual data bit + overhead data bits = 160000 bit + 8000 bit = 168000 bit
So, Efficiency = (160000/168000) × 100% = 95%

## Slide 4: Isochronous Transmission:
Isochronous transmission is similar to synchronous transmission but the time interval between blocks is almost zero.
Advantages-
Transmission speed is much higher.
There is no need to pause between each character.
Start bit at the beginning of each character and Stop bit at the end is not required.
Disadvantages-
A primary storage device is required at the sender station.
It is not possible to check whether the data block has received the correct recipient and there is no error correction.
Relatively expensive.
Uses-
This method is usually used for data transfer in real time applications.
This method is used for data transmission for various multimedia communications such as audio or video calls.

## Slide 5: Automatic Repeat ReQuest (ARQ)
Types of ARQ Protocols
There are three ARQ protocols in the data link layer.

## Slide 6: Automatic Repeat ReQuest (ARQ)
Stop – and – Wait ARQ − Stop – and – wait ARQ provides unidirectional data transmission with flow control and error control mechanisms, appropriate for noisy channels. The sender keeps a copy of the sent frame. It then waits for a finite time to receive a positive acknowledgement from receiver. If the timer expires, the frame is retransmitted. If a positive acknowledgement is received then the next frame is sent.
Go – Back – N ARQ − Go – Back – N ARQ provides for sending multiple frames before receiving the acknowledgement for the first frame. It uses the concept of sliding window, and so is also called sliding window protocol. The frames are sequentially numbered and a finite number of frames are sent. If the acknowledgement of a frame is not received within the time period, all frames starting from that frame are retransmitted.
Selective Repeat ARQ − This protocol also provides for sending multiple frames before receiving the acknowledgement for the first frame. However, here only the erroneous or lost frames are retransmitted, while the good frames are received and buffered.